| Task: | Operating a Grass/Weed Trimmer |
| --- | --- |
| Name of Shop or Dept: | Service |
| Job Title(s): | Maintenance |
| Analyzed by: | Brian Cutting |
| Date: | June 1, 2012 |
| Required PPE: |
| Safety Glasses, Ear Plugs, Work Boots, Head Cover, Proper Clothing |
| Required/Recommended Trainings: |
| Safe use of machine, First aid, PPE |
| TASK | HAZARDS | CONTROLS |
| Check Gas and Oil Mix | Injury to bystanders | Be aware of your surroundings. Safety zone is within 50 feet of another person |
| Grease and lube machine | Eye loss from thrown objects | Visually examine area remove object trimmer could throw |
| Clean air filter | Loose trimmer head or vibration | Read and understand safety manual |
| Check for loose nuts and bolts screws |  | Position body to maintain balance |
| Check fuel lines and gas tank for leaks | Cutting hand or fingers | Keep hands away from moving parts |
|  |  | Always check machine only in off position |
|  | Check for wires power cables or phone lines | Wear eye/and leg protection |
|  | Physical Condition sick taking medication or you have taken alcohol |  |