| Task: | OIL CHANGE |
| --- | --- |
| Name of Shop or Dept: | SERVICE |
| Job Title(s): | Maintenance |
| Analyzed by: |  |
| Position vehicle for lifting Date: |  |
| Required PPE: |
| CSA approved steel-toed footwear CSA approved safety glasses or goggles chemical gloves approved attire |
| Required/Recommended Trainings: |
| TASK | HAZARDS | CONTROLS |
| OIL CHANGE: 1. Inspect work area to ensure that it is free of hazards. Read appropriate MSDS prior to starting oil change. | Trip, slip, fall Fire and or explosion | Remove any clutter in work area. Practice good housekeeping prior to starting any work. Clean up spills and remove any combustible or flammable materials. Note location of nearest fire extinguisher/s and fire blanket/s. |
| 2. Vehicle is being raised by hoist; refer to manual for proper instruction for that type of vehicle. | Vehicle may fall or slide causing crushing injury or death | Refer to proper JHA for using the hydraulic car lift. Always refer to vehicle service manual and hoist manual before you lower vehicle onto safety stands. Do not work around or under a vehicle that is not secure |
| 3. Loosen but do not remove drain plug. Place waste oil recovery tank or container as close as possible to oil drain and then remove plug. When you remove the filter, there will also be oil draining or dripping from that location. If there is a large oil spill, clean it up while oil is draining | Oil can be hot causing burns. Exposure to waste oil/ petrol products may have toxic effects. Slipping on an oil spill causing injury to head and or body. | Wear your safety glasses/goggles and protective gloves. Do not get hot engine oil on your skin or clothing, if this happens remove clothing and wash skin immediately. Clean up any spills to avoid slipping and causing injury. |
| 4. Replace drain plug and new oil filter following the manufacturer’s instructions. (Remember to always hand tighten the oil filter. DO NOT USE ANY TOOLS TO TIGHTEN THE OIL FILTER). Install new oil into vehicle per vehicle service manual. Check under vehicle to make sure oil is not leaking out. Clean area of spills and recycle old oil and oil filter in appropriate storage area. | Exposure to waste oil/petrol products may have toxic effects. Improper disposal of waste oil and filter will have environmental impact. | Do not get engine oil on your skin or clothing, if this happens remove clothing and wash skin immediately. Practice good housekeeping , clean up andy spills. Follow guidelines for the recycling of waste oil and filter, also place used oil in designated area for proper disposal. |

Name (print):______________________________________________________

Position: __________________________________________________________

Date: ____________________________________________________________

Signature: ________________________________________________________